APPENDIX I.13

(See paragraph 5.6.1.1)

LAYOUT FOR THE INTERNATIONAL MARITIME METEOROLOGICAL tape (immt)

[version immt-1]

Element  Character	Code	Element	Coding procedure

Number  Number

1	1	iT	Format/temperature indicator	3=IMMT format with temperatures in tenths of °C

4=IMMT format with temperatures in halves of °C

5=IMMT format with temperatures in whole °C

2	2-5	AAAA	Year UTC	Four digits

3	6-7	MM	Month UTC	01 - 12 January to December

4	8-9	YY	Day UTC	01 - 31

5	10-11	GG	Time of observation	Nearest whole hour UTC, WMO specifications

6	12	Qc	Ouadrant of the globe	WMO code table 3333

7	13-15	LaLaLa	Latitude	Tenths of degrees, WMO specifications

8	16-19	LoLoLoLo	Longitude	Tenths of degrees

9	20		Cloud height (h) and visibility (VV)	0 - h and VV estimated

measuring indicator	1 - h measured, VV estimated

2 - h and VV measured

3 - h estimated, VV measured

10	21	h	Height of clouds	WMO code table 1600

11	22-23	VV	Visibility	WMO code table 4377

12	24	N	Cloud amount	Oktas, WMO code table 2700; show 9 where applicable

13	25-26	dd	True wind direction	Tens of degrees, WMO code table 0877; show 00 or 99

where applicable

14	27	iw	Indicator for wind speed	WMO code table 1855

15	28-29	ff	Wind speed	Tens and units of knots or metres per second, hundreds

omitted; values in excess of 99 knots are to be indicated

in units of metres per second and Iw encoded accordingly;

the method of estimation or measurement and the units

used (knots or metres per second) are indicated in

element 14

16	30	sn	Sign of temperature	WMO code table 3845

17	31-33	TTT	Air temperature	Tenths of degrees Celsius

18	34	st	Sign of dew-point temperature	0 - positive or zero measured dew-point temperature

1 - negative measured dew-point temperature

2 - iced measured dew-point temperature

5 - positive or zero computed dew-point temperature

6 - negative computed dew-point temperature

7 - iced computed dew-point temperature

19	35-37	TdTdTd	Dew-point temperature	Tenths of degrees Celsius

20	38-41	PPPP	Air pressure	Tenths of hectopascals

21	42-43	ww	Present weather	WMO code table 4677

22	44	W1	Past weather	WMO code table 4561

23	45	W2	Past weather	WMO code table 4561

24	46	Nh	Amount of lowest clouds	As reported for CL or, if no CL cloud is present, for CM,

in oktas; WMO code table 2700

25	47	CL	Genus of CL clouds	WMO code table 0513

26	48	CM	Genus of CM clouds	WMO code table 0515

27	49	CH	Genus of CH clouds	WMO code table 0509

28	50	sn	Sign of sea-surface temperature	WMO code table 3845

29	51-53	TwTwTw	Sea surface temperature	Tenth of degrees Celsius

30	54		Indicator for sea-surface	0 - Bucket thermometer

temperature measurement	1 - Condenser inlet

2 - Trailing thermistor

3 - Hull contact sensor

4 - “Through hull” sensor

5 - Radiation thermometer

6 - Bait tanks thermometer

7 - Others

31	55		Indicator for wave measurement		0 - Wind sea and swell estimated

Shipborne	1 - Wind sea and swell measured

wave	2 - Mixed wave measured, swell estimated

recorder	3 - Other combinations measured and

estimated

4 - Wind sea and swell measured

Buoy	5 - Mixed wave measured, swell estimated

6 - Other combinations measured and

estimated

7 - Wind sea and swell measured

Other	8 - Mixed wave measured, swell estimated

measurement	9 - Other combinations measured and

system	     estimated

32	56-57	PwPw	Period of wind waves or of	Whole seconds; show 99 where applicable in

measured waves	accordance with Note (3) under specification of

PwPw in the Manual on Codes

33	58-59	HwHw	Height of wind waves or of	Half-metre values. Examples: Calm or less than 1/4m

measured waves	to be encoded 00; 31/2m to be encoded 07; 7m to be

encoded 14; 111/2m to be encoded 23

34	60-61	dw1dw1	Direction of predominant	Tens of degrees, WMO code table 0877; encoded 00

swell waves	or 99 where applicable.

Blanks = No observation of waves attempted

35	62-63	Pw1Pw1	Period of predominant	Whole seconds; encoded 99 where applicable

swell waves	(see under element 32)

36	64-65	Hw1Hw1	Height of predominant swell waves	Half-metre values (see under element 33)

37	66	Is	Ice accretion on ships	WMO code table 1751

38	67-68	EsEs	Thickness of ice accretion	In centimetres

39	69	Rs	Rate of ice accretion	WMO code table 3551

40	70		Source of observation	0 - Unknown

1 - Logbook	National

2 - Telecommunication channels

3 - Publications

4 - Logbook	International

5 - Telecommunication channels	data exchange

6 - Publications

41	71		Observation platform	0 - unknown

1 - Selected ship

2 - Supplementary ship

3 - Auxiliary ship

4 - Automated station/data buoy

5 - Fixed sea station

6 - Coastal station

7 - Aircraft

8 - Satellite

9 - Others ....

42	72-78		Ship identifier	Ship’s call sign or other identifier encoded as follows:

7 characters call sign Columns 72–78

6 characters call sign Columns 72–77

5 characters call sign Columns 72–76

4 characters call sign Columns 72–75

3 characters call sign Columns 72–74

43	79-80		Country which has recruited the ship	According to numbers assigned by WMO

44	81		National use

45	82		Quality control indicator	0 - No quality control (QC)

1 - Manual QC only

2 - Automated QC only (no time-sequence checks)

3 - Automated QC only (inc. time sequence checks)

4 - Manual and automated QC (superficial; no automated

time-sequence checks)

5 - Manual and automated QC (superficial; including

time-sequence checks)

6 - Manual and automated QC (intensive, including

automated time-sequence checks)

7 & 8 - Not used

9 - National system of QC (information to be

furnished to WMO)

46	83	ix	Weather data indicator	1 - Manual

4 - Automatic	If present and past weather data included

Code tables 4677 and 4561 used

7 - Automatic	If present and past weather data included

Code tables 4680 and 4531 used

47	84	iR	Indicator for inclusion or omission	WMO code table 1819

of precipitation data

48	85-87	RRR	Amount of precipitation which has	WMO code table 3590

fallen during the period preceding

the time of observation, as indicated

by tR

49	88	tR	Duration of period of reference for	WMO code table 4019

amount of precipitation, ending at

the time of the report

50	89	sw	Sign of wet-bulb temperature	0 - positive or zero measured wet-bulb temperature

1 - negative measured wet-bulb temperature

2 - iced measured wet-bulb temperature

5 - positive or zero computed wet-bulb temperature

6 - negative computed wet-bulb temperature

7 - iced computed wet-bulb temperature

51	90-92	TbTbTb	Wet-bulb temperature	In tenths of degree Celsius, sign given by element 50

52	93	a	Characteristic of pressure tendency	WMO code table 0200

during the three hours preceding

the time of observation

53	94-96	ppp	Amount of pressure tendency at	In tenths of hectopascal

station level during the three hours

preceding the time of observation

54	97	Ds	True direction of resultant	WMO code table 0700

displacement of the ship during

three hours preceding the time of

observation

55	98	vs	Ship’s average speed made good	WMO code table 4451

during the three hours preceding

the time of observation

56	99-100	dw2dw2	Direction of secondary swell waves	Tens of degrees, WMO code table 0877;

encoded 00 or 99 where applicable.

Blanks = No observation of waves attempted

57	101-102	Pw2Pw2	Period of secondary swell waves	Whole seconds; encoded 99 where applicable

(see under element 32)

58	103-104	Hw2Hw2	Height of secondary swell waves	Half-metre values (see under element 33)

59	105	ci	Concentration or arrangement	WMO code table 0639

of sea ice

60	106	Si	Stage of development	WMO code table 3739

61	107	bi	Ice of land origin	WMO code table 0439

62	108	Di	True bearing of principal ice edge	WMO code table 0739

63	109	zi	Present ice situation and trend of	WMO code table 5239

conditions over preceding three hours

64	110		FM 13 code version	0 = previous to FM 24-V

1 = FM 24-V

2 = FM 24-VI Ext.

3 = FM 13-VII

4 = FM 13-VIII

5 = FM 13-VIII Ext.

6 = FM 13-IX

7 = FM 13-IX Ext.

8 = FM 13-X, etc.

65	111		IMMT version	0 = previous IMMT

1 = IMMT-1 (this version)

2 = IMMT-2 (next version)

3 = IMMT-3, etc.

66	112	Q1	Quality control indicator for (h)	0 - no quality control (QC) has been performed

in this element

1 - QC has been performed; element appears to be correct

2 - QC has been performed; element appears

to be inconsistent with other elements

3 - QC has been performed; element appears to be doubtful

4 - QC has been performed; element appears to be

erroneous

5 - The value has been changed as a result of QC

6 - 8 Reserve

9 - The value of the element missing

67	113	Q2	QC indicator for (VV)	- idem -

68	114	Q3	QC indicator for (clouds:	- idem -

elements 12, 24–27)

69	115	Q4	QC indicator for (dd)	- idem -

70	116	Q5	QC indicator for (ff)	- idem -

71	117	Q6	QC indicator for (TTT)	- idem -

72	118	Q7	QC indicator for (TdTdTd)	- idem -

73	119	Q8	QC indicator for (PPPP)	- idem -

74	120	Q9	QC indicator for (weather:	- idem -

elements 21–23)

75	121	Q10	QC indicator for (TwTwTw)	- idem -

76	122	Q11	QC indicator for (PwPw)	- idem -

77	123	Q12	QC indicator for (HwHw)	- idem -

78	124	Q13	QC indicator for (swell: elements	- idem -

34–36, 56–58)

79	125	Q14	QC indicator for (iRRRRtR)	- idem -

80	126	Q15	QC indicator for (a)	- idem -

81	127	Q16	QC indicator for (ppp)	- idem -

82	128	Q17	QC indicator for (Ds)	- idem -

83	129	Q18	QC indicator for (vs)	- idem -

84	130	Q19	QC indicator for (TbTbTb)	- idem -

85	131	Q20	QC indicator for ships’ position	- idem -